## Slide 1: Tool Checkout Vending Machine
May 1416

## Slide 2: The Project
Tool Checkout Vending Machine
  Similar to a library lending arrangement
  Students swipe ID and select desired product
  Tool record added to authorized student database
  Admin checks in returned tools in CSG electronic shop, modifies student database
  Admin can modify tools and edit inventory

## Slide 3: Raspberry Pi
Why?
  Needed video output for LCD on front panel
  Capable of USB attachments and hub.
  Advisor/client recommended
  Department had a spare model in stock
  Confidence in ability to work with and program

## Slide 4: Raspberry Pi
Apache Server
  Provides administrator websites
Database
  Student Information
  Tool Inventory
Python Scripts
GPIO Pins
  Motors
  Matrix Keypad

## Slide 5: LCD
Connects to RCA video output on Raspberry Pi
Displays full screen responses to user through Pygame module use
Main program code sends strings and text positions to Pygame methods to update screen

## Slide 6: Card Reader
Connects to USB port on Raspberry Pi
Reads & parses student ID (9-digit) from ISU card
Used to track users within database

## Slide 7: Failed Card Reader
Half Track Insert Reader
Worked with manufacturer to troubleshoot reading issues
Found it was unable to read full data tracks
Scrapped use in project

## Slide 8: Keypad
10-pin matrix
Connected to GPIO pins on Raspberry Pi
Functionality
  Read pressed column
  Read pressed row
  Get value from pre-determined 2d array

## Slide 9: USB Wireless Adapter
Transmits network data from Raspberry Pi to IASTATE wireless network
Uses
  SSH access to machine
  Admin webpages
  Database backups

## Slide 10: Powered USB Hub
Plugs in through standard wall adapter
Supplies power to
  Raspberry Pi
  Wireless network adapter
  Card Reader
Feeds data to computer through micro-USB cable

## Slide 11: Vending Machine Case
We were provided a used electronic snack vending machine by Lance made in 1999.
Case had suffered dents scrapes and rust. The previous lock had been forcibly removed before our possession.
Much of the internal wiring and fixtures were unnecessary for our purpose and removed.

## Slide 12: Refinishing the Case
Removed unnecessary parts
Cleaned out buildup of dirt/muck.
Used power hand grinder to smooth out jagged cuts around the lock.
Sanded with power hand sander with 100, 150, and 220 grit sandpaper.
Spray painting method was not optimal; used enamel oil-based primer and 2 gloss coats of paint, sanding with 220 grit sandpaper between coats.

## Slide 13: Front Panel
Needed a new front panel for new configuration
LCD, magnetic strip card reader, original matrix keypad.
Panel cut using CAD and metal miller, and assembled by hand.

## Slide 14: Admin – Students

## Slide 15: Admin – Machine

## Slide 16: Circuit Schematic
Original PCB design for our motor controller
Controller accepts 3.3V input directing which motor to turn and high side and low side drivers with logic input allow 24 volts to flow to the motors
Faulty hardware caused over current in the drivers often

## Slide 17: Circuit
Adapted to issues by switching to a circuit configuration using triacs.
More reliable and low current – allowed for more individual component testing and replacement.

## Slide 18: Video

## Slide 19: Logistical Challenges
Motor drivers and gpio extender
  Burnt out during testing
SD card corruption
  Rebuilt OS from recent backup
Parts reimbursement
  Individually purchased components/supplies
Machine touchups
  Difficult to work on due to weather conditions

## Slide 20: Testing Plan
Parts functionality testing
  Motors
  Screen
  Keypad
  Computer
Machine testing
  All components work together correctly
  Program does not fail over long periods of time

## Slide 21: Final Testing
Magnetic card reader software failure
  Simplified code
Database failure
  MySQL server would not start
  Removed and reinstalled, still not starting
  Implemented workaround (commented out database functions)
Keypad connections unreliable
  Wiring needed reseating occasionally
  Reboot of system

## Slide 22: Final Testing
GPIO extender burned out
  Make use of remaining GPIO pins on Raspberry Pi
LCD Screen cross-communication
  Swiping card or using keypad affects display settings
Motor harness wiring
  Contacts are larger than wires used
  Fix will be use of larger wire gauge between GPIO and motors

## Slide 23: Possible Critical Scenarios
Power Outage
  Possible SD card corruption
  Maintain OS & database backups
Documentation of equipment and supplies necessary for future scenarios such as:
  Dead equipment
  Overheating
  Vandalism

## Slide 24: End
May 1416